## Slide 1: Mintendo Swich
組員:廖耕毅 門玉仁 陳妍喻

## Slide 2: Outline
Project introduction
Project structure
Demo clips
Improvements
  Low energy consideration(ISR, sleeping mode)
  wifi session handling
  Enhancing motion detection accuracy
Conclusion
Future works

## Slide 3: Project Introduction
We intended to design stm32 as a video game controller which can easily adapt on different video games with sensitive controlling, low energy consideration and some user friendly designs.
Specifically, we will demonstrate our project on Mario kart game and pong.

## Slide 4: Project Structure and Controller Design

## Slide 5: Demo Clips – Mario Kart

## Slide 6: Demo Clips – Pong

## Slide 7: Improvements-Low Energy Design(ISR)
Purpose: pressing button triggers ISR to send data to server
Problem 1:
  Description: Bouncing -> trigger ISR multiple times with incorrect reading value
  Solution: Disable IRQ -> program order is important
Problem 2:
  Description: Multiple interruptins -> cause program malfunction
  Maybe sharing same interrupt vector -> unsolved

## Slide 8: Improvements-Low Energy Design(Sleeping Mode)
Purpose: If no motion occurs, stm32 will enter sleeping mode(e.g. not sending data to server) to save energy.
With high sensitivity, we will not miss any motion

## Slide 9: WIFI Session Handling
Purpose: handling sever client disconnection issues
Improvement 1:
  Description: stm32 lose wifi connection
  Solution: Prompt error and looping for re-connection
Improvement 2:
  Description: Can not establish server-client connection
  Solution: Prompt error and restart a new socket
Improvement 3:
  While gaming, if socket disconnect unexpectedly, the program will exit and prompt error for restarting the system

## Slide 10: Enhancing Motion Detection Accuracy
Problem: After stm32 sensor’s calibration, bias still remains.
Description: Bias are random offsets, which limits detection accuracy
Solution: Calibrate once more on server
Benefits: This greatly enhance our detection accuracy
Future work: during gaming your hand’s position will change slightly which will again affect detection accuracy -> dynamic calibration

## Slide 11: Conclusion - Project
Game controller features:
Key board manipulation:
  Easily adapt on different games
  Avoid game looping asynchronous problem
Low energy consideration
  ISR
  Sleeping mode
Wifi reconnection designs
Precise motion detection
Manageable OOP design
server
client

## Slide 12: Conclusion – Used Course Materials
Interrupt Service Routine
bouncing handling
Event and eventqueue
Sensor node
Wifi and client socket server

## Slide 13: Future Works
Multiple Interruptins implementation
Dynamic calibration

## Slide 14: Thanks For Your Attention