## Slide 1: Mintendo Swich
組員:廖耕毅 門玉仁 陳妍喻

## Slide 2: Outline
Project introduction
Project structure
Demo clip
Improvement
  Low energy consideration(ISR, sleeping mode)
  wifi session handling
  Precise motion detection handling
Conclusion
Still existing problems

## Slide 3: Project Introduction
We intended to design stm32 as a video game controller which can easily adapt on different video games with sensitive controlling, low energy consideration and some user friendly designs.
Specifically, we will demonstrate our project on Mario kart game and pong.

## Slide 4: Project Structure and Controller Design

## Slide 5: Demo Clips – Mario Kart

## Slide 6: Demo Clips – Pong

## Slide 7: Improvements-Low Energy Design(ISR)
Purpose: pressing button triggers ISR to send data to server
Problem 1:
  Description: Bouncing -> trigger ISR multiple times with incorrect reading value
  Solution: Disable IRQ -> program order is important
Problem 2:
  Description: Multiple interruptins -> cause program malfunction
  Maybe sharing same interrupt vector -> unsolved

## Slide 8: Improvements-Low Energy Design(Sleeping Mode)
Purpose: If no motion occurs, stm32 will enter sleeping mode(e.g. not sending data to server) to save energy.
With high sensitivity, we will not miss any motion

## Slide 9: WIFI Session Handling
Purpose: sending data to server for further keyboard control
Preliminary steps
  Try to connect to wifi until succeed
  Try to connect to socket until succeed
    If socket cannot connect, delete the old socket and build a new socket
Data processing
  Send data
    If socket disconnect unexpectedly, the program will exit and need to restart
    If no motion, the program will stop to send data until motion occur

## Slide 10: Precise Motion Detection Handling
Problem: After stm32 sensor’s calibration, bias still remains.
Description: Bias are random offsets, which hugely limits detection accuracy
Solution: Calibrate once more on server
Benefits: This greatly enhance our detection accuracy
Future work: during gaming your hand’s position will change slightly which will again affect detection accuracy -> dynamic calibration

## Slide 11: Conclusion - Project
Key board manipulation:
  Easily adapt on different games
  Avoid game looping asynchronous problem
Low energy consideration
  ISR
  Sleeping mode
Wifi reconnection design
Precise motion detection
Manageable OOP design
Server
client

## Slide 12: Conclusion – Used Course Materials
Interrupt Service Routine
bouncing handling
Event and eventqueue
Sensor node
Wifi and client socket server

## Slide 13: Still Existing Problems
Multiple Interruptins implementation
Dynamic calibration

## Slide 14: Thanks For Your Attention